## Slide 1: Malware in IEEE 802.11 Wireless Networks
Brett Stone-Gross*, Christo Wilson*,
Kevin Almeroth*, Elizabeth Belding*, Heather Zheng*,
and Konstantina Papagiannaki**
*Department of Computer Science,
University of California, Santa Barbara
**Intel Research
Pittsburgh, PA

## Slide 2: Scenario
Connecting to a wireless LAN
  Users have become accustomed to protection from
    NATs
    Firewalls
  Worms and bots actively scan the Internet for vulnerable hosts
    Identify machines via port scans
    Attack/Exploit

## Slide 3: Outline
Objectives
Motivation & Applicability
Experimental Setup
Identifying Malicious Flows
MAC Layer Impacts
Overall Impacts
Conclusions & Future Work

## Slide 4: Objectives
To quantify, characterize, and correlate the effects of malicious traffic flows on a wireless LAN.
This is the first study to analyze these effects in a large-scale wireless network
  More resource limitations
    Bandwidth
    Channel access

## Slide 5: Motivation & Applicability
Improve quality of service offered by wireless networks
Assist in developing more realistic traffic models that account for malicious traffic
Applicable to almost any wireless network, especially those with lax security constraints including wireless hotspots
Substantiate the need for better wireless network protections

## Slide 6: Experimental Setup
  Data collection from the 67th IETF meeting in San Diego, California for a 5-day duration
  44.7Mbps T3 backhaul link
  Publicly routable subnet 130.129/16
    No network address translation (NAT)
  No firewall/MAC layer encryption
  30 access points
    802.11a/b/g
  11 wireless packet sniffers
    IBM/Toshiba laptops with Atheros chipsets
  Wired and wireless traffic captured from a trunk port on the core router

## Slide 7: Wireless Sniffer Locations

## Slide 8: Data Collection Statistics
Wired Data Set
  Packet traces from all hosts over all 5 days
  511GB uncompressed
Wireless Data Set
  Packet traces from 11 concurrent access points
  131 GB uncompressed
The wired data set was initially utilized to identify malicious flows and then matched with the smaller wireless data set

## Slide 9: Detecting Malicious Flows
Port scanning & flooding
Large numbers of short-lived connections
  TCP SYNs, ICMP ping
Well-known exploit signatures
  Port-based
  Malicious payloads
Since nearly all connected machines were laptops, unsolicited incoming connections to various services were easily identifiable

## Slide 10: Most Common Malicious Flows
HTTP TCP SYN floods
NetBIOS/Microsoft Discovery Services exploits
SSH brute force dictionary attacks
MS SQL exploits

## Slide 11: Malware-Driven Traffic Flows
TCP Statistics
  Egress
    4,076,412 out of 272,480,816 (1.5%) were classified as malicious
  Ingress
    2,765,683 out of 284,565,595 (1.0%) were classified as malicious
3,906 out of 109,740 unique external IP addresses (3.6%) engaged in malicious traffic flows
14 out of 1,786 internal IP addresses (0.8%) showed indications of malicious activity.
  Network experts are more security conscious? 
  At least one person was likely infected at the conference

## Slide 12: Malicious Ingress Flows
Not ideal for studying the MAC layer effects
  Attacks that involved only a few total packets
  Few services were running on connected hosts (mostly laptops)
Natural load-balancing
  Port scans that were distributed over hosts on all 30 access points
  Backscatter from DoS attacks throughout the Internet that produced unsolicited TCP SYN ACKs, resets, and ICMP replies also distributed over all 30 access points

## Slide 13: Malicious Egress Flows
Ideal for studying effects of malware attacks
  All packets are broadcasted and processed by a single access point
  Broadcasts impact nearby hosts
    Channel Busy-time/Utilization
    Packet collisions
      Management frames
      Data frames
  Transmission rates
    Auto-Rate Fallback (ARF) mechanism
      Reduces transmission rates in favor of more robust modulation and coding schemes

## Slide 14: MAC Layer Impact Summary
Increased
  Number of data retransmissions
  Channel utilization
  Probe requests
Reduced
  Transmission rates
    11-18Mbps rates increased while 48-54Mbps rates decreased significantly
  Probe responses

## Slide 15: Case Study
ICMP ping in combination with a NetBIOS worm exploit that originated from a single machine on the wireless LAN
  78,295 overall packets in about 18 minutes
  Start: 17:02:38
  End: 17:20:45
  Attack halted for about 2 minutes at 17:09:00
  Bursts of 235 packets per second
  Average rate of 117 packets per second

## Slide 16: MAC Layer Impact-Data Retries

## Slide 17: MAC Layer Impact- Channel Utilization

## Slide 18: MAC Layer Impact-Probe Responses

## Slide 19: MAC Layer Impact- ARF Responses

## Slide 20: Overall Impact
Increased round-trip-times (RTTs)
 | Non-Attack Interval | During Attack | Percent Increase
Average Egress | 64.7 ms | 99.2 ms | 53.2%
Avg Ingress | 23.4 ms | 36.1 ms | 54.4%
Median Egress | 41.6 ms | 85.0 ms | 104.3%
Median Ingress | 3.2 ms | 6.8 ms | 112.5%

## Slide 21: Conclusions
Malicious traffic flows have a detrimental impact on wireless networks
  MAC Layer
  Latency/Round-trip-time
Auto-rate fallback is not optimal during congested intervals
The mechanism of probing for better connectivity may only increase overall network contention
  Probe responses and other management frames may be blocked during periods of high channel utilization

## Slide 22: Future Work
Aggregate statistics for similar data sets
  IETF data sets
    58th, 60th, 62nd, 64th
  Trend Analysis
    Malicious flows
    Evolution of malware
    Backscatter analysis
Network Protection Solutions
  How to filter this traffic? How much of an impact will this make?
Traffic Modeling with Malicious Flows

## Slide 23: Questions?
Contact Information
  Email: bstone@cs.ucsb.edu